## Slide 1: Lab Equipment
A guide to the things you’ll soon be breaking

## Slide 2: Let’s learn about lab equipment!
I’m not going to define what lab equipment is, because you can probably figure that out for yourself.
But there will be a quiz on it.

## Slide 3: 1) Equipment for holding stuff
Beaker:
An all-purpose device for holding things and doing reactions.
Warnings:
The numbers on the side are approximate (probably correct within 10%). Don’t use them to find the volume of a liquid.
Don’t heat a beaker unless there’s a liquid still in it. Otherwise, it will shatter.

## Slide 4: Erlenmeyer Flask
Uses:
Pretty much the same things as a beaker are used for, but generally better to keep liquids from splashing when heated.
Warnings:
Like a beaker, you shouldn’t heat them until they go dry and you shouldn’t use the markings on the side to find the volume of a liquid.

## Slide 5: Electronic balance
What it is, how to use it:
Used to weigh things.
Hit the “tare” button before weighing to zero it out.
Use a watch glass to weigh dry chemicals.
Don’t do these things:
Don’t weigh things directly on the balance.
Don’t weigh hot things on it because it will melt.
Don’t push down on it because it will break.

## Slide 6: Watch glass
Uses:
Weighing chemicals on the balance
Covering heated beakers to keep things from splashing out of them.
Fun facts:
Watch glasses get their name from the fact that they look like the glass that covers the face of a watch.
They look like big contact lenses.

## Slide 7: 2) Equipment used for heating things
Ring stand, ring, and wire gauze
Ring stand:
The thing in the picture with the dark base and the metal rod that points straight up.
Used primarily when heating chemical compounds over a Bunsen burner (the Bunsen burner sits on the dark base)
Ring:
A metal ring that clamps to the ring stand. Primarily used to hold the…
Wire gauze:
…upon which you put the container to be heated.

## Slide 8: Bunsen burner
Uses:
To make things really hot.
Other info:
The Bunsen burner on the left is a traditional burner, shown here under a ring stand of a different variety.
The Bunsen burner on the right is a portable version, which we currently use because the gas in our lab doesn’t work.

## Slide 9: Crucible and evaporating dish
Crucible with lid
Evaporating dish
Uses:
Both of these ceramic bits of equipment are used to heat chemicals to very high temperatures over the Bunsen burner.
How to use:
Crucibles are placed over Bunsen burners in the clay triangle placed on the ring.
Evaporating dishes are placed directly on wire gauze.
Warnings:
If you put them directly from the heat into water, they will break. Wait at least 10 minutes before doing this.

## Slide 10: Crucible Tongs
Crucible tongs are used to carry crucibles from one place to another.
Alternate use: To directly hold objects over a Bunsen burner.
The figures here show the correct way to carry a crucible with crucible tongs.

## Slide 11: Clay triangle: Good for heating crucibles
If you want to heat a crucible over the Bunsen burner, don’t use a wire gauze – it will fall over and break. Why not instead nestle it in a clay triangle?

## Slide 12: 3) Tools for moving things around
spatula
scoopula
The spatula and the scoopula are both used for essentially the same thing – moving dry chemicals from bottles to wherever the reaction will occur.

## Slide 13: Graduated Cylinder
You know how I told you that you shouldn’t use a beaker or Erlenmeyer flask to find the volume of fluids? Well, this is the equipment you should use.

## Slide 14: Beaker tongs
Beaker tongs are used to move beakers from one place to another, typically while they’re hot.
The correct use of beaker tongs is shown to the left.

## Slide 15: Stirring rod
Glass rods used for stirring.
Note: Never use thermometers as stirring rods, because they’ll break.

## Slide 16: Safety equipment
Goggles must be worn at all times in the lab.
Regular glasses are not a substitute for goggles unless you’ve gotten them with special chemical and impact resistant lenses.

## Slide 17: Fume Hood
Fume hoods are workbenches that have fans over them which blow chemical fumes through a chemical scrubber.
The fume hoods work, but you have to let them run for a moment before they turn on. If you wait for a humming sound, you’ll be in good shape.

## Slide 18: Safety shower and eyewash
The safety shower is used to wash off large amounts of chemical that have spilled on you. It’s also handy to put you out if you’re on fire.
The eyewash is used to wash foreign materials out of your eyes, in the event that you have a chemical accident while not wearing goggles. Handy tip: If you need to use an eyewash, there’s an excellent chance that it’s too late to save your eyes.
eyewash

## Slide 19: Fire blanket
If you catch on fire, you can smother it with a fire blanket.
As with the safety shower and eyewash, if you need this piece of equipment, you’re already in very serious trouble.

## Slide 20: 4) Other equipment
You can filter the solid from a solution by pouring it through a filter paper that’s been placed in a funnel.

## Slide 21: Thermometer
I know that you know what a thermometer is. I just wanted this to be a reminder to never use them to stir solutions.

## Slide 22: In conclusion
There will be a quiz on this stuff, so know it.